## Slide 1
WORKBOOK AI · MODULE A7 EXTENSION
From toy fabric to training-grade fabric
Designing a 3-spine, 9-leaf, 15-host fat-tree topology for OpenSM training
Spine · Leaf · Host — proportional tiers of a non-blocking Clos fabric
Built on real ibsim + OpenSM 3.3.23 · PA-ALT-N11

## Slide 2
RECAP
The current lab proves the mechanism, not the discipline
What you built (Module A7)
OpenSM (MASTER)
| LD_PRELOAD (libumad2sim.so)
ibsim -- Switch1 (LID 2, 8 ports)
|-- port 1 -- Hca1 (LID 1)
|-- port 4 -- Hca2 (LID 3)
1 switch, 2 hosts, 1 path
sminfo, ibstat, ibnetdiscover all confirmed working end to end against real OpenSM output.
What it can't teach
Multiple switches or tiers
Fat-tree / Clos routing
Path diversity, failover
Partitioned fabrics (P_Keys)
SM redundancy and handover
Congestion, oversubscription
Module A7 (baseline) — 3-node topology
2

## Slide 3
CONCEPT
Why fat-tree is the industry-standard AI/HPC fabric shape
A fat-tree (a Clos-derived topology) is the design pattern behind essentially every large InfiniBand and RoCEv2 AI cluster in production.
Switches are organized into tiers
— spine at the top, leaf below it, hosts at the bottom — with every leaf connected to every spine.
This gives
non-blocking, multi-path connectivity: any host can reach any other host, and if one spine fails, the Subnet Manager reroutes across the survivors — the exact failure-recovery behavior Exercise 4 puts to the test.
Spine 1
Spine 2
Spine 3
Leaf 1
Leaf 2
Leaf 3
Hca
Hca
Hca
Hca
Hca
Hca
Every leaf uplinks to every spine — the full pattern (9 leaves, 15 hosts) follows the same rule
Concept — Clos / fat-tree architecture
3

## Slide 4
THE BUILD
3 spines · 9 leaves · 15 hosts
Non-blocking fat-tree, 3:1 oversubscription at the spine layer
3
Spine switches
LID 4-6
9
Leaf switches
LID 7-15
15
Hosts (HCAs)
LID 16-30
27
Total nodes
in one topology file
Naming convention
S<n> = Spine switch (S1..S3)
L<n> = Leaf switch (L1..L9)
H<n> = Host / HCA (H1..H15)
File
~/ibsim-lab/fat-tree.net
Same net-file grammar as mytopo.net
(Switch / Hca blocks, port lines)
4

## Slide 5
REFERENCE
Topology file — spine and leaf excerpt
Full file: ~/ibsim-lab/fat-tree.net (27 node blocks). Same syntax you already tested in mytopo.net.
Switch 8 "S1" # Spine-1, LID 4
[1] "L1"[1]
[2] "L2"[1]
[3] "L3"[1] ... [8] "L8"[1]
Switch 8 "L1" # Leaf-1, LID 7
[1] "S1"[1]
[2] "S2"[1]
[3] "S3"[1]
[4] "H1"[1] ... [8] "H5"[1]
Hca 2 "H1" # Host-1, LID 16
[1] "L1"[4]
Reading it
Each Switch/Hca block declares its own ports.
Port lines are symmetric — S1 port 1 to L1 port 1 must be echoed by L1 port 1 to S1 port 1. LIDs shown are the expected pattern — OpenSM assigns the real ones on discovery, same as it did for mytopo.net.
Reference — fat-tree.net excerpt
5

## Slide 6
CURRICULUM
Seven sessions, roughly four and a half hours total
SESSION
FOCUS
TIME
1
Start fat-tree, observe discovery, ibnetdiscover
30 min
2
ibroute inspection — understand computed paths
30 min
3
Multi-SM failover (priority, handover)
45 min
4
Partitioning with P_Keys
45 min
5
Failure scenarios — remove a spine
45 min
6
LMC and multi-pathing
45 min
7
Congestion — conceptual, tie back to Workbook AI A2-A5
30 min
Curriculum — recommended progression
6

## Slide 7
EXERCISE 1
Observe fat-tree routing
Start OpenSM against the new topology and watch it discover 27 nodes instead of 3.
cd ~/ibsim-lab
ibsim -r -l 12345 -s ./fat-tree.net
# terminal 2 — SIM_HOST must match a real node in fat-tree.net
export SIM_HOST="H1"
LD_PRELOAD=.../libumad2sim.so opensm -g 0 -f ./osm.log
Questions to answer
Which HCA does OpenSM pick as SM master?
How many hops between H1 and H15?
What path does OpenSM choose? (check osm.log)
NOT YET TESTED HERE
Command shape matches A7's proven pattern, but this specific topology and SIM_HOST value have not been run in this lab yet.
Exercise 1 of 7
7

## Slide 8
EXERCISE 2
Route inspection with ibroute
Dump the real computed routing table and inspect the path between two specific hosts.
LD_PRELOAD=... SIM_HOST=H1 ... ibroute
# path to H15 (LID 30)
LD_PRELOAD=... SIM_HOST=H1 ... ibroute -D 30
LD_PRELOAD=... SIM_HOST=H1 ... ibnetdiscover
Questions to answer
Does the printed path match your prediction from the diagram?
Is the route symmetric in both directions?
NOT YET TESTED HERE
ibroute is a real infiniband-diags tool (same package as ibnetdiscover), but this exact invocation is unverified in this lab.
Exercise 2 of 7
8

## Slide 9
EXERCISE 3
Partitioning with P_Keys
P_Keys are InfiniBand's VLAN equivalent — isolating groups of hosts at the fabric level.
# /etc/opensm/partitions.conf (real, confirmed path
# from this lab's own opensm --create-config dump)
Partition "AI-Training" pkey=0x8001 : H1,H2,...,H10
Partition "Management" pkey=0x8002 : H11,...,H15
Questions to answer
What happens when H1 tries to reach H11?
Is the failure silent or does the fabric report it explicitly?
NOT YET TESTED HERE
partition_config_file is a real, confirmed OpenSM setting (seen in this lab's own dumped config). The exact syntax above is illustrative — verify against the real file format before use.
Exercise 3 of 7
9

## Slide 10
EXERCISE 4
Failure domain analysis
Comment out Spine-2 entirely and redeploy — a controlled failure, not a crash.
# edit fat-tree.net: remove the S2 block
# and every [n] "S2"[m] reference in the leaves
ibsim -r -l 12345 -s ./fat-tree.net
# restart OpenSM the same way as Exercise 1
Questions to answer
Does the fabric still work with 2 of 3 spines?
Which HCAs, if any, lose connectivity?
Does OpenSM reconverge on its own, or does it need a nudge?
NOT YET TESTED HERE
Directly exercises the same route-recompute logic already proven working in A7.8 (minhop tables configured on all switches) — mechanism is proven, this specific scenario is not yet run.
Exercise 4 of 7
10

## Slide 11
EXERCISE 5
Multi-subnet — SM redundancy
Run two OpenSM instances at different priorities and force a handover.
# terminal 2 — primary, priority 0
LD_PRELOAD=... opensm -g 0 -f ./osm.log -p 0
# terminal 3 — secondary, priority 1, different host
export SIM_HOST="H2"
LD_PRELOAD=... opensm -g 0 -f ./osm2.log -p 1
Questions to answer
Which instance becomes MASTER?
What happens the moment the master is stopped?
How long does failover actually take?
TESTED IN THIS LAB
--priority / -p is a real, confirmed flag — read directly from this lab's own captured opensm --help output on day one. Running two instances together is untested.
Exercise 5 of 7
11

## Slide 12
EXERCISE 6
LMC — multi-path LIDs
LID Mask Control lets one physical port hold multiple LIDs, enabling several paths per host.
# in fat-tree.net:
Switch 8 "S1" lmc 1
Switch 8 "S2" lmc 1
Switch 8 "S3" lmc 1
Questions to answer
How does LID assignment change once lmc is set?
Does ibroute now show multiple valid paths per host pair?
NOT YET TESTED HERE
Whether ibsim's topology parser accepts an inline "lmc" field on the Switch header line is UNCONFIRMED — this lab has already seen ibsim reject unexpected line syntax ("cannot parse remote lid and connection type", A7.7). Test the parse before trusting the exercise.
Exercise 6 of 7
12

## Slide 13
EXERCISE 7
Congestion — conceptual
Drop to 2 spines under the same host count to model 3:1 oversubscription, without moving real data.
# thought experiment / topology edit only —
# no new tool, reasoning exercise
# ties directly back to Workbook AI Module A2-A5
# (PFC, ECN, DCQCN) — same fabric, real dataplane
Questions to answer
How does 2-spine oversubscription change bisection bandwidth?
Which host pairs are affected first?
How would PFC/ECN behave here, per Workbook AI Module A2-A5?
TESTED IN THIS LAB
This exercise is explicitly conceptual, same tier as Module A4's DCQCN discussion — no dataplane test is claimed or possible with ibsim.
Exercise 7 of 7
13

## Slide 14
MASTERY MAP
What each exercise actually teaches
CONCEPT
HOW IT'S DEMONSTRATED
WHERE
Fat-tree architecture
3 spines, 9 leaves — non-blocking Clos
Ex. 1
LID assignment
Predictable pattern across 27+ nodes
Ex. 1
OpenSM routing
Real computed tables via ibroute
Ex. 2
Path diversity
Multiple valid paths, host to host
Ex. 2, 6
Failure recovery
Remove a spine, watch reconvergence
Ex. 4
SM redundancy
Priority-based master handover
Ex. 5
Partitioning
P_Key isolation between groups
Ex. 3
LMC / multi-path
One port, multiple LIDs
Ex. 6
Congestion reasoning
Oversubscription, tie to PFC/ECN
Ex. 7
Mastery map — concept to exercise
14

## Slide 15
READ BEFORE YOU RUN ANYTHING
Verified fact vs. proposed exercise — know the difference
Same evidence discipline as the rest of this workbook: nothing here is trusted until it's actually been run and checked.
OK
ibsim -r -l <port> -s <file>
Confirmed working (A7.7-A7.9) — same syntax, new topology file
OK
opensm -g <hex> -f log -B
Confirmed working with a real GUID — daemon mode included
OK
--priority / -p <n>
Confirmed real flag, read from this lab's own opensm --help
OK
sminfo / ibstat / ibnetdiscover with the LD_PRELOAD wrapper
Confirmed working end to end, today
!
"-v 2" verbosity flag (as pasted in the source material)
CONTRADICTS this lab's own captured --help output — no lowercase -v exists. Use -V or -D <level> instead.
!
ibroute
Real infiniband-diags tool, but not yet run in this lab
!
Inline "lmc 1" on a Switch header line
Unconfirmed whether ibsim's parser accepts this field at all
!
Two simultaneous OpenSM instances (Exercise 5)
Mechanism is plausible; multi-instance coordination is untested here
15

## Slide 16
SUMMARY
Low pedagogical ceiling to realistic fabric design
ASPECT
BASELINE (A7)
FAT-TREE (THIS DECK)
Nodes
3 (1 switch, 2 HCAs)
27 (3 spines, 9 leaves, 15 HCAs)
Paths between hosts
Exactly 1
Multiple, via ibroute
Failure domains
None
Spine and leaf, independently
Partitioning
Not applicable
P_Keys, real config path
SM redundancy
Not applicable
Priority + handover
Routing complexity
Trivial
Realistic, Clos-based
16

## Slide 17
Next action
Build fat-tree.net, run it once, verify the unverified
1. Write fat-tree.net from Slide 5's pattern, all 27 blocks.
2. Run Exercise 1 exactly as shown — confirm discovery before anything else.
3. Fix the "-v 2" flag before you type it.
4. Treat every amber item on Slide 15 as a hypothesis, not a fact, until you've run it.
Workbook AI · Module A7 Extension · PA-ALT-N11